## Slide 1: Biosignal Processing
July 28, 2022

## Slide 2
Physiological Energy
Transducer
Amplifier
Analog-Digital Converter
Signal Processing
Feature Extraction
Classification
Accurate Biosignal Representation Starts with Processing
Computer
Measuring Equipment

## Slide 3
Physiological Energy
Transducer
Amplifier
Analog-Digital Converter
Signal Processing
Feature Extraction
Classification
Accurate Biosignal Representation Starts with Processing
Computer
Measuring Equipment

## Slide 4
01
Signal
Sampling
Workshop Objectives
02
Time and
Frequency Domains
04
Filtering
03
Noise

## Slide 5
Part 1:
Signal Sampling

## Slide 6
Continuous System
Discrete Representation
Notes: Neural signals, whether they are representative of neural activity in a single neuron, the heart, or brain exist on a continuous plane meaning that between any two sampled time points, there are an infinite number of data points that exist. We are limited by computational speed, ability, and memory therefore, we cannot realistically measure these continuous signals. Rather, we must represent them as samples of their continuous form.
Biosignals are represented by a continuous range of voltages, can take on an infinite number of possible values.
Computers are digital and can only acquire discrete voltage levels at discrete timepoints

## Slide 7
Continuous System
Discrete Representation
Reconstruct the continuous signal
(with infinite # of possible values)
using digital signals (finite # of possible values)
Notes: Neural signals, whether they are representative of neural activity in a single neuron, the heart, or brain exist on a continuous plane meaning that between any two sampled time points, there are an infinite number of data points that exist. We are limited by computational speed, ability, and memory therefore, we cannot realistically measure these continuous signals. Rather, we must represent them as samples of their continuous form.
Biosignals are represented by a continuous range of voltages, can take on an infinite number of possible values.
Computers are digital and can only acquire discrete voltage levels at discrete timepoints

## Slide 8
Sampling Rate
Sample the continuous signal at discrete time points at a constant rate (sampling frequency)
Connect the discrete voltage values at the sampled times to reconstruct/represent continuous signal

## Slide 9
Sampling Rate
How do we know if our sampling rate accurately represents our measured signal?

## Slide 10
Sampling Rate
How do we know if our sampling rate accurately represents our measured signal?
The Nyquist Theorem!

## Slide 11
Nyquist Theorem
We must sample a signal at a rate that is at least 2x higher than the highest frequency in the signal

## Slide 12
Nyquist Theorem
We must sample a signal at a rate that is at least 2x higher than the highest frequency in the signal
Let’s practice choosing our sampling frequency!

## Slide 13
Nyquist Theorem
We must sample a signal at a rate that is at least 2x higher than the highest frequency in the signal
Example 1: We want to measure a Human ECG signal (heart activity). The clinically defined signal bandwidth is 0.05-100 Hz. What should our sampling frequency be?

## Slide 14
Nyquist Theorem
We must sample a signal at a rate that is at least 2x higher than the highest frequency in the signal
Example 2: We want to measure the alpha wave activity in an EEG signal. What is the signal bandwidth? What is the minimum sampling frequency to accurately represent the signal?

## Slide 15
Nyquist Theorem
We must sample a signal at a rate that is at least 2x higher than the highest frequency in the signal
What happens if we sample below the Nyquist frequency?

## Slide 16
Aliasing and the Nyquist Theorem
Aliasing!

## Slide 17
Aliasing and the Nyquist Theorem
Aliasing!
https://www.youtube.com/watch?v=yr3ngmRuGUc

## Slide 18
Activity 1: ECG signal and Aliasing

## Slide 19
Activity 1: ECG signal and Aliasing
2000 Hz
200 Hz
200 Hz

## Slide 20
Why not always have a high sampling frequency?
Can reconstruct the original signal accurately
Have to store a lot of data (Need more storage space)
Have to collect & save the data quickly
(Need high processing power)

## Slide 21
Part 2:
Time and Frequency Domain
Notes: Now that we have sampled our signal and reconstructed it, let’s consider how we can visualize our signal in both the time and frequency domains

## Slide 22
Time and Frequency Domains
Notes: We learned that fundamentally a signal is characterizing a process as a function of the other. Specifically, we look at the relationship between an independent and dependent variable. However, particularly in the case

## Slide 23
Time and Frequency Domains
https://www.youtube.com/watch?v=fYtVHhk3xJ0

## Slide 24
Time and Frequency Domains
How do we interpret complex signals in the frequency domain?
Notes: We learned that fundamentally a signal is characterizing a process as a function of the other. Specifically, we look at the relationship between an independent and dependent variable. However, particularly in the case

## Slide 25
Time vs. Frequency Domain
D
F
B

## Slide 26
Time vs. Frequency Domain
D
F
B
Fast Fourier Transform (fft)

## Slide 27
Activity 2: Identify Frequency Components using fft()

## Slide 28
Activity 2: Identify Frequency Components using fft()
Time Domain
Frequency Domain
Time Domain

## Slide 29
Aliasing in the Frequency Domain?
Notes: I will not go into the mathematical detail behind the algorithm (you can do that outside this course) but to convert between time and frequency you use fft()

## Slide 30
Part 3:
Noise
Notes: Now that we have sampled our signal and reconstructed it, let’s consider how we can visualize our signal in both the time and frequency domains

## Slide 31
Physiological Energy
Transducer
Amplifier
Analog-Digital Converter
Signal Processing
Feature Extraction
Classification
Noise affects all parts of acquisition
Computer
Measuring Equipment
Noise!
Noise!
Noise!
Notes: Especially for biosignals, noise is an important consideration because it can affect all aspects of acquisition. With biosignals being on the order of uV, if we do not eliminate noise in our signal, it will quickly drown out what we are trying to measure

## Slide 32
Sources of Noise
Measurement noise from:
Electrodes
  Movement, coupling to skin changes
  Thermal noise àcaused by thermal agitation of electrons in a conductor
Electronic components in the measurement circuit
  Amplifiers, resistors, etc each contribute some noise to the signal
Electrical sources in the surrounding environment
  e.g. 60 Hz AC noise from power lines, fluorescent lights

## Slide 33
Sources of Noise
60Hz noise (Mains Hum)

## Slide 34
Sources of Noise
White noise

## Slide 35
Sources of Noise
Physiological Noise
e.g. heart rate or respiration in MRI

## Slide 36
Sources of Noise
Motion Artifact

## Slide 37
Activity 3: How does noise affect our signal in time and frequency domains?

## Slide 38
“Respiration” (Physiological) noise
No Noise
Amp = 0.1
Amp =1
Amp = 10

## Slide 39
Mains Hum
No Noise
Amp = 0.1
Amp =1
Amp = 10

## Slide 40
White Noise
No Noise
Amp = 0.1
Amp =1
Amp = 10

## Slide 41
Part 4:
Filtering

## Slide 42
Noise can easily be identified in the frequency domain

## Slide 43
How can we remove noise?
Digital Filters can be used to eliminate noise
Notch filter….

## Slide 44
Example: “Respiration” (Physiological) noise
No Noise
Amp =1

## Slide 45
Example: Mains Hum
No Noise
Amp =1

## Slide 46
How do Filters work?
Impulse response is the filter response in the time domain

## Slide 47
How do Filters work?
Convolution

## Slide 48
How do Filters work?
FIR and IIR filters
https://community.sw.siemens.com/s/article/introduction-to-filters-fir-versus-iir

## Slide 49
Filter Design Considerations: Filter Types

## Slide 50
Filter Design Considerations: Filter Order

## Slide 51
Activity 4: Let’s build filters and apply them!

## Slide 52
Activity 4: Let’s build filters and apply them!
Fc1 = 10 Hz; fc2 = 30 Hz; order = 2
Fc1 = 18 Hz; fc2 = 22 Hz; order = 2
Fc1 = 18 Hz; fc2 = 22 Hz; order = 6